## Slide 1: FFT Audio Visualizer
Rehan Iqbal
Yogesh Dhada
Meng Lei

## Slide 2: Block Diagram
Audio Input (Nexys4 Microphone)
audio demo
FFT
Image Control
VGA Display
DTG
Nexys4_RGB_if
pushbuttons
Picoblaze

## Slide 3: Audio_demo
Dedicated ADC on Nexys4DDR board samples at 3MHz
Provides PDM output of sample

## Slide 4: Audio_demo: main I/O
.clk_i
.clk_6_144MHz
.pdm_data_i
.pdm_clk_o
.data_mic_valid
.data_mic
pdm_filter
.pdm_lrsel_o

## Slide 5: Pulse Density Modulation
Increasing number of 1’s as signal amplitude increases

## Slide 6: PDM Filter
Noise Problem:
  Crappy mic
4 filter stages
  CIC Filter
  Highband filter
  Lowpass filter
  Highpass filter
Low-pass FIR filter
Notes: CIC works 192Khz
Second stage: Halfband filter with decimation ratio of 2 and input -- sampling frequency of 192 kHz, resulting in a 96 kHz output sample rate.
Low pass filter: sampling rate 96KHz
HighPass 96KHz removing DC component

## Slide 7: pdm_filter: main I/O
.clk_i
.clk_6_144MHz
.pdm_data_i
.pdm_clk_o
.fs_o
.data_o
CIC filter
halfband filter
lowpass filter
highpass filter

## Slide 8: Dividing the 6.144MHz clock for 3.072MHz

## Slide 9: CIC Filter:
A twist on the recursive running-sum filter
  Which is a twist on the moving average

## Slide 10: Fast Fourier Transform
Use Cooley–Tukey FFT algorithm to split Discrete Fourier Transform into multiple smaller DFT’s
  This reduces operation order from O (n ^ 2) to O( n * log n )
  Multiple forms: different radices, butterfly options, etc.
  Lends itself to parallel computation

## Slide 11: First attempt: use HLS to implement
Multiple high-level synthesis (HLS) tools available:
  System Generator: design and simulate using Simulink blocks specifically made for Vivado
  HDL Coder: write MATLAB code or design Simulink and convert to HDL
  Vivado HLS: write C code and convert to HDL
Issues: Need to compare generated HDL against original model
  Fixed point conversion issues
  Checking whether it’s accurate enough
  Simulation speed (co-simulate on board possible)
  Just getting familiar with workflow is hard

## Slide 12: Two Vivado IP cores available
Discrete Fourier Transform
Fast Fourier Transform

## Slide 13: ImgControl
Similar to icon.v from Project 2
  Store FFT output in a block RAM
  As pixel goes across screen, read memory to find FFT power reading for that bin
  Based on vertical position and power, determine whether to draw or not